## Slide 1: Microprocessor Systems and Interfacing CPE 342
Lecture 2- Week 4

## Slide 2: PPI Applications
Outline
  Mode 0 Operation :Interfacing Stepper Motor

## Slide 3: Stepper Motor Interface
Stepper motor is digital in nature
It rotates in a sequence of discrete steps controlled by sequentially energizing a set of coils (windings)
Step angles vary from 1o to 15o depending on precision required (and cost)
ROL= Motor rotates anticlockwise
ROR= Motor rotates clockwise
0 | 0 | 1 | 1

## Slide 6: Stepper Motor
Wave Drive.
Signal sequence for Wave Drive Stepping Mode |  |  |  | 
Step | Yellow lead (End point 1 of Phase1) | Blue lead (End point 2 of Phase1) | Red lead (End point 1 of Phase2) | White lead (End point 2 of Phase2)
1 | 1 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0
3 | 0 | 1 | 0 | 0
4 | 0 | 0 | 0 | 1

## Slide 7: Stepper Motor
Full Drive.
Signal sequence for Full Drive Stepping Mode |  |  |  | 
Step | Yellow lead (End point 1 of Phase1) | Blue lead (End point 2 of Phase1) | Red lead (End point 1 of Phase2) | White lead (End point 2 of Phase2)
1 | 1 | 0 | 1 | 0
2 | 0 | 1 | 1 | 0
3 | 0 | 1 | 0 | 1
4 | 1 | 0 | 0 | 1

## Slide 8: Stepper Motor
Half Drive.

## Slide 9: Stepper Motor
Half Drive.
Signal sequence for Half Drive Stepping Mode |  |  |  | 
Step | Yellow lead (End point 1 of Phase1) | Blue lead (End point 2 of Phase1) | Red lead (End point 1 of Phase2) | White lead (End point 2 of Phase2)
1 | 1 | 0 | 0 | 0
2 | 1 | 0 | 1 | 0
3 | 0 | 0 | 1 | 0
4 | 0 | 1 | 1 | 0
5 | 0 | 1 | 0 | 0
6 | 0 | 1 | 0 | 1
7 | 0 | 0 | 0 | 1
8 | 1 | 0 | 0 | 1

## Slide 10: Task
Modify the code to operate the stepper motor in half step mode.