## Slide 1: Microprocessor Systems and Interfacing CPE 342
Lecture 1- Week 5

## Slide 2: PPI Applications
Outline
  Mode 0 Operation :LCD Interfacing with PPI

## Slide 7
EXAMPLE 11–12
PORTA_ADDRESS EQU 700H ;set port addresses
PORTB_ADDRESS EQU 701H
COMMAND_ADDRESS EQU 703H
;macro to send a command or data to the LCD display
;
SEND MACRO PORTA_DATA, PORTB_DATA, DELAY
MOV AL,PORTA_DATA ;PORTA_DATA to Port A
MOV DX,PORTA_ADDRESS
OUT DX,AL
MOV AL,PORTB_DATA ;PORTB_DATA to Port B
MOV DX,PORTB_ADDRESS
OUT DX,AL
OR AL,00000100B ;Set E bit
OUT DX,AL ;send to Port B
AND AL,11111011B ;Clear E bit
NOP ;a small delay
NOP
OUT DX,AL ;send to Port B
MOV BL,DELAY ;BL = delay count
CALL MS_DELAY ;ms Time Delay
ENDM

## Slide 8
;Program to initialize the LCD display
START:
MOV AL,80H ;Program the 82C55
MOV DX,COMMAND_ADDRESS
OUT DX,AL
MOV AL,0
MOV DX,PORTB_ADDRESS ;Clear Port B
SEND 30H, 2, 16 ;send 30H for 16 ms
SEND 30H, 2, 5 ;send 30H for 5 ms
SEND 30H, 2, 1 ;send 30H for 1 ms
SEND 38H, 2, 1 ;send 38H for 1 ms
SEND 8, 2, 1 ;send 8 for 1 ms
SEND 1, 2, 2 ;send 1 for 2 ms
SEND 0CH, 2, 1 ;send 0CH for 1 ms
SEND 6, 2, 1 ;send 6 for 1 ms