## Slide 1: Lec 2: DT Systems Overview
Dr. Arsla Khan

## Slide 2: Chapter 2: Overview (SNS Revision)

## Slide 5: Types of Systems
Continuous Time System
    Systems in which input and output, both signals are continuous in nature.
    e.g. Audio and video amplifier, power supplies etc.
Discrete Time System
    Systems in which input and output, both signals are discrete in nature.
    e.g. microprocessors, shift registers

## Slide 6: Interconnection of Systems
Systems can be interconnected in multiple ways
    1) Series(Cascaded) Interconnection
        Output of system 1 is input of other system
        Overall impulse response is equal to convolution of individual impulse responses.

## Slide 7
2) Parallel Interconnection
    Same input is applied to all systems.
    Overall impulse response is equal to addition of individual impulse responses
3) Series/Parallel Interconnection
    Combination of series and parallel combination

## Slide 8
4) Feedback Interconnection
    Output of system 1 is the input to system 2, while the output of system 2 is fed back and added to the external input to produce the actual input to system 1.

## Slide 9: Exp 7.1: Write relationship between input and output signals
Multiple input by 2 
Square of input 
Relationship is:

## Slide 11: 1) Causal and Non-Causal Systems
Response of the causal system to an input does not depend on future values of that input but depends only on the present and past values.

## Slide 12
Exp1:
Solution:
Put different values of in above equation to check whether it is causal or not
    Put
    Put
    Put n
is depending on previous and present values of only so it is a non-causal system

## Slide 13
Exp2:
Solution:
Put different values of in above equation to check whether it is causal or not
    Put
    Put
    Put
is depending on previous and present values of only so it is a causal system

## Slide 14
Static systems are also known as memoryless systems
Static systems contain no storage elements (thus, no integrals, derivatives or signal delays)
A static or memoryless system is a system with an output signal whose values depends upon the present value of the input signal only. Otherwise the system is dynamic or with memory.
2) Static (memoryless) and Dynamic (with memory) Systems

## Slide 15
(ii)
Solution:
Put different values of in above equation to check whether it is static or not
    Put n
    Put
    Put
is depending on previous and present of values only so it is a dynamic system

## Slide 16
A system is time invariant if the time shift in the input signal results in corresponding time shift in the output.
Let i.e. is response of Then if is delayed by time then output will also be delayed by the same time. i.e.
3) Time Invariant and Time Variant Systems

## Slide 17: Steps to test for time invariance property
Step 1: Determine the output of system for delayed input i.e.
Step 2: Then delay the output itself by i.e.
Step 3: If
     Time variant
     Time invariant

## Slide 18
Step 1: Determine the output for delayed input i.e. .
Step 2: Now delay the output by . Hence we have to replace by
Step 3: Compare with
Both are not same so system is time variant

## Slide 19: 4) Linear and Non-Linear Systems
A system is said to be linear if it follows the superposition principle.
Consider two systems defined as
    i.e. is input and is output
    i.e. is input and is output
Discrete time system is said to be linear if

## Slide 20
If  Linear

## Slide 22: Exp 8.1: Check whether the system is linear or not
For RHS
Consider two systems
For LHS
(
Since  Linear

## Slide 23: 5) Stable and Unstable Systems
When every bounded input produces bounded output. It is called Stable System.
Follows BIBO
If
Then O/P is
Bounded Input
Bounded Output

## Slide 62: Thank You !!!