## Slide 1: Microprocessor Systems and Interfacing EEE 342
Nesruminallah
nesruminallah@cuilahore.edu.pk

## Slide 2: Stack
Outline
  Stack
  Stack Programming in assembly language
CLO | Bloom Taxonomy | Specific Outcome
CLO1 | C4 | Analyze and construct the stack memory map using the knowledge of stack programming concepts

## Slide 3: Stack
Stack
  Access is allowed only at one point of the structure, normally termed the top of the stack
  access to the most recently added item only
Operations are limited:
  push (add item to stack)
  pop (remove top item from stack)
Described as a "Last In First Out" (LIFO) data structure

## Slide 4: Stack

## Slide 5: Stack

## Slide 6: Stack

## Slide 7: CPU’s stack grows downward
Stack
stack
contents
top-of-stack
0000
FFFF

## Slide 8: A Software Implementation
Data items don't move in memory, just our idea about there the TOP of the stack is.
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
TOP
/ / / / / /
/ / / / / /
/ / / / / /
#18
/ / / / / /
TOP
#12
#5
#31
#18
/ / / / / /
TOP
#12
#5
#31
#18
/ / / / / /
TOP
Initial State
After
One Push
After Three
More Pushes
After
Two Pops
x4000
x3FFF
x3FFC
x3FFE

## Slide 9: Stack Pointer
It is a 16-bit register, contains the address of the data item currently on top of the stack.
Stack operation includes pushing (providing) data on to the stack and popping (taking)data from the stack.
Pushing operation decrements stack pointer and Popping operation increments stack pointer. i.e there is a last in first out (LIFO) operation.

## Slide 10: Push
Source can be register, segment register or memory.
This instruction pushes the contents of specified source on to the stack.
In this stack pointer is decremented by 2.
The higher byte data is pushed first (SP-1).
Then lower byte data is pushed (SP-2).
  E.g.:
  (1). PUSH AX;
  (2). PUSH DS;
  (3). PUSH [5000H];

## Slide 11: Push
INITIAL POSITION
DECREMENTS SP & STORES HIGHER BYTE
HIGHER BYTE
DECREMENTS SP & STORES LOWER BYTE
LOWER BYTE
HIGHER BYTE
(1) STACK POINTER
(2) STACK
POINTER
(3) STACK POINTER

## Slide 12: Push
BH |  | BL | 
CH | 10 | CL | 50
DH |  | DL | 
BH |  | BL | 
CH | 10 | CL | 50
DH |  | DL | 
50
10
SP | 2002H
SP | 2000H
BEFORE EXECUTION
AFTER EXECUTION
2000H
2001H
2002H
2000H
2001H
2002H
PUSH CX

## Slide 13: Pop
Destination can be register, segment register or memory.
This instruction pops (takes) the contents of specified destination.
In this stack pointer is incremented by 2.
The lower byte data is popped first (SP+1).
Then higher byte data is popped (SP+2).
  E.g.
  (1). POP AX;
  (2). POP DS;
  (3). POP [5000H];

## Slide 14: Pop
INITIAL POSITION AND READS LOWER BYTE
LOWER BYTE
HIGHER BYTE
INCREMENTS SP & READS HIGHER BYTE
LOWER BYTE
HIGHER BYTE
INCREMENTS SP
LOWER BYTE
HIGHER BYTE
(1) STACK
POINTER
(2) STACK
POINTER
(3) STACK POINTER

## Slide 15: Pop
BH |  | BL | 
BH | 10 | BL | 50
SP | 2000H
SP | 2002H
50
10
50
10
BEFORE EXECUTION
AFTER EXECUTION
POP BX
2000H
2001H
2002H
2000H
2001H
2002H

## Slide 16: PUSH Example

## Slide 17: POP Example

## Slide 18: Stack Example
MOV DX, 0FFFEH
MOV SP,DX
MOV DX,0A000H
MOV SS,DX
MOV AX,0ACADH
MOV BX,1000H
PUSH AX
PUSH BX
ADD AX,BX
PUSH AX
POP CX
POP DX
HLT